## Slide 1: QoS and Impairments
Muhammad Mateen Yaqoob
Department of Computer Science
COMSATS Institute of Information Technology, Abbottabad

## Slide 2: QoS and Impairments
There are a number of generic impairments that will directly or indirectly affect quality of service
An understanding of these impairments is extremely important if one wants to grasp the entire picture of a telecommunication system

## Slide 3: QoS: Voice, Image and Data
SNR (Signal to Noise Ratio)
  It is expressed in dB
  Amount by which signal level exceeds noise level in a speciﬁed bandwidth
  Voice = 40 dB, Video (TV) = 45 dB, Data ~ 15 dB

## Slide 4: QoS: Voice, Image and Data
Loudness Rating
  Distant talker’s voice was not loud enough at receiving telephone
  Overall Loudness Rating (OLR)
  It is assumed that telephone sensitivity, both for the earpiece and microphone, have been measured
  Deﬁned as loudness loss between speaking subscriber’s mouth and listening subscriber’s ear via a telephone connection

## Slide 5: QoS: Voice, Image and Data
Bit Error Rate (BER)
  QoS parameter for data circuits
  ITU recommends a BER of 1x10-6

## Slide 6: Basic Impairments
There are three basic impairments found in all telecomm transmission systems
Amplitude (or attenuation) distortion;
Phase distortion; and
Noise

## Slide 7: Amplitude Distortion
IEEE deﬁnes attenuation distortion (amplitude distortion) as the change in attenuation at any frequency w.r.t reference frequency
Voice channel occupies band from 300 Hz to 3400 Hz (pass-band)
It can be avoided if all frequencies within pass-band are subjected to the same loss (or gain)
ITU recommends 800 Hz as the reference; in North America the reference is 1000 Hz